## Slide 1
THREE-DIMENSIONAL FORCE SYSTEMS
  In-class Activities:
  Check Homework
  Reading Quiz
  Applications
  Equations of Equilibrium
  Concept Questions
  Group Problem Solving
  Attention Quiz
Today’s Objectives:
Students will be able to solve 3-D particle equilibrium problems by
a) Drawing a 3-D free body diagram, and,
b) Applying the three scalar equations (based on one vector equation) of equilibrium.

## Slide 2
READING QUIZ
1. Particle P is in equilibrium with five (5) forces acting on it in 3-D space. How many scalar equations of equilibrium can be written for point P?
A) 2 B) 3 C) 4
D) 5 E) 6
2. In 3-D, when a particle is in equilibrium, which of the following equations apply?
  A) ( Fx) i + ( Fy) j + ( Fz) k = 0
  B)  F = 0
  C)  Fx =  Fy =  Fz = 0
  D) All of the above.
  E) None of the above.
Notes: Answers:
1. B
2. D

## Slide 3
APPLICATIONS
You know the weight of the electromagnet and its load. But, you need to know the forces in the chains to see if it is a safe assembly. How would you do this?

## Slide 4
APPLICATIONS (continued)
This shear leg derrick is to be designed to lift a maximum of 200 kg of fish.
How would you find the effect of different offset distances on the forces in the cable and derrick legs?
Offset distance

## Slide 5
THE EQUATIONS OF 3-D EQUILIBRIUM
This vector equation will be satisfied only when
Fx = 0
Fy = 0
Fz = 0
These equations are the three scalar equations of equilibrium. They are valid for any point in equilibrium and allow you to solve for up to three unknowns.
When a particle is in equilibrium, the vector sum of all the forces acting on it must be zero ( F = 0 ) .
This equation can be written in terms of its x, y and z components. This form is written as follows.
( Fx) i + ( Fy) j + ( Fz) k = 0

## Slide 6
EXAMPLE I
1) Draw a FBD of particle O.
2) Write the unknown force as
F5 = {Fx i + Fy j + Fz k} N
3) Write F1, F2 , F3 , F4 and F5 in Cartesian vector form.
4) Apply the three equilibrium equations to solve for the three
unknowns Fx, Fy, and Fz.
Given: The four forces and geometry shown.
Find: The force F5 required to keep particle O in equilibrium.
Plan:

## Slide 7
EXAMPLE I (continued)
F4 = F4 (rB/ rB)
= 200 N [(3i – 4 j + 6 k)/(32 + 42 + 62)½]
= {76.8 i – 102.4 j + 153.6 k} N
F1 = {300(4/5) j + 300 (3/5) k} N
F1 = {240 j + 180 k} N
F2 = {– 600 i} N
F3 = {– 900 k} N
F5 = { Fx i – Fy j + Fz k} N
Solution:

## Slide 8
Equating the respective i, j, k components to zero, we have
Fx = 76.8 – 600 + Fx = 0 ; solving gives Fx = 523.2 N
Fy = 240 – 102.4 + Fy = 0 ; solving gives Fy = – 137.6 N
Fz = 180 – 900 + 153.6 + Fz = 0 ; solving gives Fz = 566.4 N
Thus, F5 = {523 i – 138 j + 566 k} N
Using this force vector, you can determine the force’s magnitude and coordinate direction angles as needed.
EXAMPLE I (continued)

## Slide 9
EXAMPLE II
1) Draw a free body diagram of Point A. Let the unknown force magnitudes be FB, FC, FD .
2) Represent each force in its Cartesian vector form.
3) Apply equilibrium equations to solve for the three unknowns.
Given: A 600 N load is supported by three cords with the geometry as shown.
Find: The tension in cords AB, AC and AD.
Plan:

## Slide 10
FB = FB (sin 30 i + cos 30 j) N
= {0.5 FB i + 0.866 FB j} N
FC = – FC i N
FD = FD (rAD /rAD)
= FD { (1 i – 2 j + 2 k) / (12 + 22 + 22)½ } N
= { 0.333 FD i – 0.667 FD j + 0.667 FD k } N
FBD at A
FC
FD
A
600 N
z
y
30˚
FB
x
1 m
2 m
2 m
EXAMPLE II (continued)

## Slide 11
Solving the three simultaneous equations yields
FC = 646 N (since it is positive, it is as assumed, e.g., in tension)
FD = 900 N
FB = 693 N
y
Now equate the respective i , j , k components to zero.
 Fx = 0.5 FB – FC + 0.333 FD = 0
 Fy = 0.866 FB – 0.667 FD = 0
 Fz = 0.667 FD – 600 = 0
FBD at A
FC
FD
A
600 N
z
30˚
FB
x
1 m
2 m
2 m
EXAMPLE II (continued)

## Slide 12
CONCEPT QUIZ
1. In 3-D, when you know the direction of a force but not its magnitude, how many unknowns corresponding to that force remain?
A) One B) Two C) Three D) Four
2. If a particle has 3-D forces acting on it and is in static equilibrium, the components of the resultant force ( Fx,  Fy, and  Fz ) ___ .
A) have to sum to zero, e.g., -5 i + 3 j + 2 k
B) have to equal zero, e.g., 0 i + 0 j + 0 k
C) have to be positive, e.g., 5 i + 5 j + 5 k
D) have to be negative, e.g., -5 i - 5 j - 5 k
Notes: Answers:
1. A
2. B

## Slide 13
1) Draw a free body diagram of Point A. Let the unknown force magnitudes be FB, FC, F D .
2) Represent each force in the Cartesian vector form.
3) Apply equilibrium equations to solve for the three unknowns.
GROUP PROBLEM SOLVING
Given: A 3500 lb motor and plate, as shown, are in equilibrium and supported by three cables and d = 4 ft.
Find: Magnitude of the tension in each of the cables.
Plan:

## Slide 14
W = load or weight of unit = 3500 k lb FB = FB(rAB/rAB) = FB {(4 i – 3 j – 10 k) / (11.2)} lb
FC = FC (rAC/rAC) = FC { (3 j – 10 k) / (10.4 ) }lb
FD = FD( rAD/rAD) = FD { (– 4 i + 1 j –10 k) / (10.8) }lb
GROUP PROBLEM SOLVING (continued)
FBD of Point A
y
z
x
W
FB
FC
FD

## Slide 15
GROUP PROBLEM SOLVING (continued)
The particle A is in equilibrium, hence
FB + FC + FD + W = 0
Now equate the respective i, j, k components to zero (i.e., apply the three scalar equations of equilibrium).
 Fx = (4/ 11.2)FB – (4/ 10.8)FD = 0
 Fy = (– 3/ 11.2)FB + (3/ 10.4)FC + (1/ 10.8)FD = 0
 Fz = (– 10/ 11.2)FB – (10/ 10.4)FC – (10/ 10.8)FD + 3500 = 0
Solving the three simultaneous equations gives the tension forces
FB = 1467 lb
FC = 914 lb
FD = 1420 lb

## Slide 16
ATTENTION QUIZ
2. In 3-D, when you don’t know the direction or the magnitude of a force, how many unknowns do you have corresponding to that force?
A) One B) Two C) Three D) Four
1. Four forces act at point A and point A is in equilibrium. Select the correct force vector P.
A) {-20 i + 10 j – 10 k}lb
B) {-10 i – 20 j – 10 k} lb
C) {+ 20 i – 10 j – 10 k}lb
D) None of the above.
z
F3 = 10 lb
P
F1 = 20 lb
x
A
F2 = 10 lb
y
Notes: Answer
1. D
2. C

## Slide 17
End of the Lecture
Let Learning Continue